## Slide 1
ADAPter: Power Efficient Model Inference on Nvidia GPUs
Motivation
Tune the constants currently in use
Batching requests and test with “bursty” traffic
Integrate logic within the triton inference server code
Incorporate learned frequency floor & ceiling for each model
Incorporate model selection with different quantization
Related work
ADAPter
Growing popularity of AI models +17 billion mobile devices on the planet (~2 devices/person) = High demand for power
Efficient energy consumption for inference on such devices is crucial
More focus has been on efficient training, but NVIDIA and Amazon both estimate that inference accounts for 90% of the costs for deployed models
Most of the research focus has been on improving efficiency during model training
Estimates on cost of inference have been done by J. Barr and McDonald J. et al. Clearly demonstrating the need for more efficient approaches
Samuel S. Ogden and Tian Guo created "MODI" targeting efficient inference using edge computing
Our Approach
  Make the inference server SLO aware by forcing client to specify a desired latency with the payload.
  Method used must be quick and minimally impede inference jobs
  Uses a simple moving average to estimate whether to step up or step-down GPU frequency
  At low frequencies, requests will be dropped; use the queues to retry with exponential backoff
  We will build middleware that sits between the clients and the Triton Server that measures average deviation and tunes frequency every few seconds.
Contributions / WIP
Ante Tonkovic-Capin, Ashu Kumar, Drishan Poovaya, Pratik Sanghavi
Early results
Frequency Controller adjusts the GPU frequency to ensure that inference is served efficiently
Challenges
Initial project focused on Zeus package and research on Qualcomm Innovators Development Kit (QIDK) with Snapdragon SoC, however the device and kit was never received
Project goals modified several times as alternate approaches using available devices faced several obstacles
Even with access, modifying device hardware parameters such as power consumption can be indeterministic and difficult to validate, with other settings such as fan and cooling systems being out-of-reach completely.
Push a constant stream of inference jobs with a fixed latency comparing default versus ADAPter GPU consumption
Power draw reduces with our simple module with variance of latency increased. This happens because at lower frequencies, we go for multiple rounds of retry and backoff, frequency floor set to improve this behavior